## Slide 2
Outline
PCR Introduction and Unified Framework
Kinetic Model of PCR
Kinetic Analysis of Simplex PCR – Geometric Growth
Optimal Control of PCR
Conclusions.

## Slide 3
Outline
PCR Introduction and Unified Framework
Kinetic Model of PCR
Kinetic Analysis of Simplex PCR
Optimal Control of PCR
Conclusions.

## Slide 4
Nobel Prize - One of the most cited papers in Science Journal (~17000 in 26 years)
Central technology of modern microbiology.
Diagnosis, Genome Sequencing, Personalized Medicine, Evolutionary Studies etc.
Global PCR market - $27.4 billion by 2015*.
Polymerase Chain Reaction
* On line summary of PCR in medical application – (2009 – 2015)
Notes: Polymerase Chain Reaction is a DNA amplification Reaction. It was invented by Kary Mullis in 1987 and he won the Nobel prize for this. After getting rejected from Nature Journal, this work got published in Science which eventually got cited around 16,000 times so far in last 25 years.
Thermal Cycler is a device which is used to conduct PCR reactions. This reaction is a work horse of every modern biochemistry and molecular biology labs for various research Application. Few main applications includes: Diagnosis, Genome sequencing, Personalized medicine and Evolutionary studies.
Though it is very important, it suffers to amplify specific genes, in particular, genes that has more GC content.

## Slide 5
DNA Melting
Primer
Annealing
Single Strand – Primer Duplex
Extension
DNA Melting
Again
Notes: PCR is a cyclic process and each cycle consists of 3 steps.
1st Step is called as a melting step in which double stranded DNA is separated in to two single strand DNA. This step occurs relatively at a higher temperature (mostly at 90 deg C). A chemical reaction for this step is written as –
2nd Step is called as a Annealing step in which a small single strand primer molecule hybridized on a specific spot on a single strand molecule at relative lower temperature. Primer molecules are designed in such a way that it can hybridize on the single strand molecule. There are two types of primer molecules for two single strands and their hybridization reaction is represented as. Note that single strands can also hybridize each other at lower temperature as per this reaction but the primer concentration is kept in excess so that primer annealing dominates the single strands annealing – Towards the end of the PCR this is not the case.
3rd Step is enzymatic extension of the partially completed Single stranded primer duplex to convert it in to a complete double strand DNA. An enzyme called Taq polymerase which is even active at 72 deg C, binds on the SP molecule and add the nuclo-bases on it to convert in to a DNA. The Michalis Menton based Reaction is given as:
As we can see here at the end of three steps we got 2 DNAs from 1 DNA and now we will repeat for n cycles and after n cycles we will get 2^n. n is typically 25 to 30. Thus using PCR we get million copies of DNA from 1 DNA.
The temperature vs time profile that is typically followed for this reaction is indicated by blue line. This may or may not optimal. We look for a tempeature profile which optimizes the DNA concentration. Possibly something like which is indicated in brown line.

## Slide 6
Variants of PCR – Heuristic Approach
Last two decades several new PCR have been proposed – Heuristic approach
Two step PCR1
1. Skladny et al, Journal of Clinical Microbiology (1999), 37, 3865 - 3871
Notes: In this slide, we discuss how PCR is used in Cancer Diagnostics, which is one of the most important applications of the PCR. A person who has cancer can have two types of DNA. The first one is wild type DNA and the second one is mutated DNA. As we know, mutated DNA causes the Cancer. The aim is now to find out whether a person has mutated DNA or not. if yes, how much is the concentration of such a DNA. If we can amplify the mutated DNA, it is possible to back calculate the amount of original DNA. So, here one can post an Optimization problem with an Objective : Maximize the concentration of mutated DNA. Note that we also have a wild type DNA. Change the reaction environment in such a way that, it maximizes the concentration of mutated DNA. Analogy can be made with exiting process in a tight parking spot. The plot suggest a such a possible reaction condition. While the blue one maximizes the wild type DNA, red one suppose to maximize the concentration of mutated DNA. What could be the optimal reaction condition that maximizes the mutated DNA concentration . Probably the brown one. One need to formulate an optimization problem systematically and solve. This study can also be used to monitor the performance of cancer treatment.

## Slide 7
Variants of PCR – Heuristic Approach
Last two decades several new PCR have been proposed – Heuristic approach
Two step PCR1
COLD PCR2 in Cancer Diagnosis
2. Jin et al, Nature Medicine (2008), 14, 579 – 584
Notes: In this slide, we discuss how PCR is used in Cancer Diagnostics, which is one of the most important applications of the PCR. A person who has cancer can have two types of DNA. The first one is wild type DNA and the second one is mutated DNA. As we know, mutated DNA causes the Cancer. The aim is now to find out whether a person has mutated DNA or not. if yes, how much is the concentration of such a DNA. If we can amplify the mutated DNA, it is possible to back calculate the amount of original DNA. So, here one can post an Optimization problem with an Objective : Maximize the concentration of mutated DNA. Note that we also have a wild type DNA. Change the reaction environment in such a way that, it maximizes the concentration of mutated DNA. Analogy can be made with exiting process in a tight parking spot. The plot suggest a such a possible reaction condition. While the blue one maximizes the wild type DNA, red one suppose to maximize the concentration of mutated DNA. What could be the optimal reaction condition that maximizes the mutated DNA concentration . Probably the brown one. One need to formulate an optimization problem systematically and solve. This study can also be used to monitor the performance of cancer treatment.

## Slide 8
Variants of PCR – Heuristic Approach
Last two decades several new PCR have been proposed – Heuristic approach.
Two step PCR1
COLD PCR2 in Cancer Diagnosis
Rapid PCR3
3. Wittwer CT, Garling DJ (1991) BioTechniques 10: 7683
Notes: In this slide, we discuss how PCR is used in Cancer Diagnostics, which is one of the most important applications of the PCR. A person who has cancer can have two types of DNA. The first one is wild type DNA and the second one is mutated DNA. As we know, mutated DNA causes the Cancer. The aim is now to find out whether a person has mutated DNA or not. if yes, how much is the concentration of such a DNA. If we can amplify the mutated DNA, it is possible to back calculate the amount of original DNA. So, here one can post an Optimization problem with an Objective : Maximize the concentration of mutated DNA. Note that we also have a wild type DNA. Change the reaction environment in such a way that, it maximizes the concentration of mutated DNA. Analogy can be made with exiting process in a tight parking spot. The plot suggest a such a possible reaction condition. While the blue one maximizes the wild type DNA, red one suppose to maximize the concentration of mutated DNA. What could be the optimal reaction condition that maximizes the mutated DNA concentration . Probably the brown one. One need to formulate an optimization problem systematically and solve. This study can also be used to monitor the performance of cancer treatment.

## Slide 9
Unified Framework
Heuristic Approaches – In the absence of Predictive model
Requires a large number of experiments – Expensive and time consuming.
Huge variation in the composition of target DNA – Each target DNA in principle constitutes a new PCR.
Can all of these and other reactions be unified under one principle?
A general approach to dynamic optimization of DNA amplification has applications to the design of new types of amplification reactions, in addition to enhancement of existing reactions.
Notes: In this slide, we discuss how PCR is used in Cancer Diagnostics, which is one of the most important applications of the PCR. A person who has cancer can have two types of DNA. The first one is wild type DNA and the second one is mutated DNA. As we know, mutated DNA causes the Cancer. The aim is now to find out whether a person has mutated DNA or not. if yes, how much is the concentration of such a DNA. If we can amplify the mutated DNA, it is possible to back calculate the amount of original DNA. So, here one can post an Optimization problem with an Objective : Maximize the concentration of mutated DNA. Note that we also have a wild type DNA. Change the reaction environment in such a way that, it maximizes the concentration of mutated DNA. Analogy can be made with exiting process in a tight parking spot. The plot suggest a such a possible reaction condition. While the blue one maximizes the wild type DNA, red one suppose to maximize the concentration of mutated DNA. What could be the optimal reaction condition that maximizes the mutated DNA concentration . Probably the brown one. One need to formulate an optimization problem systematically and solve. This study can also be used to monitor the performance of cancer treatment.

## Slide 10
Objective - Optimization Framework
Systems Biology Approach
First Principle Modeling of system
Deterministic Optimization
Quantitative Prescription of cycling protocol (Temperature vs Time) – There is no method so far.
Modify the existing temperature protocol to improve the amplification efficiency.
Sequence-dependent control law &
Control of geometric growth.

## Slide 11
Kinetic Model – Literature Review
Sequence independent Annealing Modeling
Craig et al (1971) , J. Mol. Bio
Porschke and Eigen (1971) – J. Mol. Bio
Equilibrium Thermodynamics of Enzyme Binding
Datta and LiCata (2003),
Nucleic Acids Research
Temperature independent Kinetics of Extension Reaction for Non – Taq Enzymes
Kuchta at al (1987), Biochemistry
Hung, M., N. Arnheim, and M. Goodman. (1992), Nucleic Acids Research
Sequence and Temperature independent PCR Model
Mehra and Hu (2005), Biotechnology Bioengineering
Stolovitzky and Cecchi (1996), PNAS
Gevertz et al (2005) - Biotechnology Bioengineering
Notes: There is no sequence and temperature dependent kinetic model for PCR. Few work was done on a specific type of DNA.
No optimal control frame work to optimize PCR have been presented so far.

## Slide 12
Kinetic Model – Literature Review
There is no Optimal Control Framework on this Problem
Sequence and Temperature Independent PCR model
Thermodynamically Inconsistent
Optimization Framework can’t be developed
Notes: There is no sequence and temperature dependent kinetic model for PCR. Few work was done on a specific type of DNA.
No optimal control frame work to optimize PCR have been presented so far.

## Slide 13
Objectives & Approach
PCR Model
Melting
Annealing
Enzyme Binding and Extension
Optimal Control
Objective: Maximize the Desired DNA Concentration
Model
Optimal Control Solver
Optimal Reaction Condition
Sequence and Temperature dependent Kinetic Model
Notes: Thus, the following goals to maximize the DNA concentration should be attained.

## Slide 14
Outline
PCR Introduction and Unified Framework
Kinetic Model of PCR
Kinetic Analysis of Simplex PCR
Optimal Control of PCR
Conclusions.

## Slide 15
Kinetic Model (Annealing/Melting)
ΔG – From Well Established Nearest Neighbor Method (Theoretical)
Reaction
Equilibrium Information
PCR operating condition is currently chosen only based on the above thermodynamic method.
Notes: The annealing Reaction is –
Equilibrium relationship for this reaction is written as
Gibbs free energy is estimated using well established Nearest Neighbor method – This is sequence dependent model that estimates the Gibbs free energy.
We have only one relationship for the forward and reverse rate constant.
Second relationship can be obtained from the relaxation time. Relaxation is similar to the time constant in Process control. Perturb the equilibrium and measure the time that is taken for the system to reach the equilibrium.
Solve both equations to obtain the forward and reverse reaction constant.
Experimentally relation time can be estimated! We can’t do this for every DNA sequence. A theoretical method is required!!

## Slide 16
Kinetic Model (Annealing/Melting)
Solve above equations to obtain rate constants
Relaxation Time – Measure of Kinetics
Similar to the Time constant in Process Control
Experimental Estimation of Relaxation time (Stopped Flow Apparatus) is time consuming and expensive.
Theoretical Estimation of Relaxation time is preferable.
Sequence dependent Predictive Model to estimate relaxation time
Notes: The annealing Reaction is –
Equilibrium relationship for this reaction is written as
Gibbs free energy is estimated using well established Nearest Neighbor method – This is sequence dependent model that estimates the Gibbs free energy.
We have only one relationship for the forward and reverse rate constant.
Second relationship can be obtained from the relaxation time. Relaxation is similar to the time constant in Process control. Perturb the equilibrium and measure the time that is taken for the system to reach the equilibrium.
Solve both equations to obtain the forward and reverse reaction constant.
Experimentally relation time can be estimated! We can’t do this for every DNA sequence. A theoretical method is required!!

## Slide 17
Hybridization /Melting–Mechanism
Schwarz Jr and Poland (1975), JCP
Two sided modified melting theory.
Identify the rate limiting step and hence the relaxation time.
Notes: We propose a theoretical method to estimate the relaxation time from the reaction mechanism of annealing reaction.
Each step of the above mechanism represent the formation of a single (hybridization) bond.
The parameter sigma accounts for the resistance for the formation of the first bond. The ratio of the forward and reverse rate constant is called as stability constant and it can be estimated using the NN. Each bond will have a separate stability constant.
The forward rate constant is assumed to be a constant (This is an assumption based on the work Wetmur and Craig) – This need to be experimentally validated.
Reverse state constant can be determined from the stability constant.

## Slide 18
Relaxation time – Exact Model
State Space Representation
Negative reciprocal of the maximum Eigenvalue is the Relaxation time.
N = 2
Temperature and sequence length dependent model parameters have been estimated using known relaxation time.
Marimuthu and Chakrabarti (2014), JCP, (Accepted)
Notes: Exact Model – Form a state space matrix
Eigenvalue of the matrix A will give the several time constant – The negative reciprocal of the maximum eigenvalue is the dominating time constant or the relaxation time.

## Slide 19
Relaxation Time Model Parameters
Sequence and Temperature Dependent Model Parameters
Marimuthu and Chakrabarti (2014), JCP, (Accepted)

## Slide 20
Estimation of Annealing Rate Constants
Start
Specify the Sequence and Temperature
Calculate ΔG using NN
Obtain the Relaxation time model Parameters
Calculate K and Equilibrium Concentration
Obtain K and τ
Solve the above equations
Construct the State Space
Eigen Decomposition
Notes: Exact Model – Form a state space matrix
Eigenvalue of the matrix A will give the several time constant – The negative reciprocal of the maximum eigenvalue is the dominating time constant or the relaxation time.

## Slide 21
Experimental Validation
Our model matches with the
experimental results
Marimuthu and Chakrabarti (2014), JCP, (Accepted)
Applications other than PCR
Micro array. (Multiplex frame work)
Southern blot.
This frame work can be extended to
Multiplex hybridization reactions
Hybridization with mismatches
Cancer
Diagnosis
Notes: Figure compares the rate constants that are estimated experimentally and theoretically. It can be see that, there is only minor difference between the rate parameters that are obtained experimentally and theoretically.
This figure shows the evolution of SP molecules that was obtained using the experimentally estimated and theoretically estimated rate constants.
Thus, our theoretical model predicts the rate parameters properly.

## Slide 22
Kinetic Model (Enzyme Binding & Extension)
ENZYME BINDING
EXTENSION
Notes: Enzyme binding reaction is represented as—
Equilibrium thermodynamics is well established by Datta and Licata at various temperature.
We need one more relationship.
Can be obtained from the relaxation time and the value is available for a same family of the enzyme at 20 deg C. We assume the same value for all other temperature. Relaxation time does not vary much with respect to temperature (Same order of magitude).
Hence, found the rate constants at various temperatures (Need to validate this assumption experimentally).

## Slide 23
Reaction Mechanism
E + Di E.Di + dNTP E.Di.dNTP E’.Di.dNTP
k1
k-1
k2
k-2
k3
k-3
E+Di+dNTP
k7
E+Di+dNTP
k8
k-4
k4
E’.Di+1.PPi
k-5
k5
E.Di+1.PPi
k-6
k6
E.Di+1+PPi
k1
k-1
E+Di+1
Step 1
Step 2
Step 7
Step 8
Step 5
Step 6
Per Nucleobase Addition
E +Di+1 + PPi
k-1
k1
E.Di + dNTP
k1
k-1
E+Di
E.Di .dNTP
k2
k-2
kcat
E.Di+1 + PPi
Simplified
Michaelis Menten Kinetics
Step 3
Step 4
Brown et al (2009), Hung, M., N. Arnheim, and M. Goodman. (1992)

## Slide 24
Experimental Estimation of Extension
Rate Constants
Measured the initial rate at different substrate (N0) concentration
Parameters are estimated using Non linear Parameter estimation
Marimuthu et al., Biophysical J (Under Review)
Notes: Extension reaction of single nucleotide insertion is represented by----
The rate equation can be derived ----
Innis et al determined the number of nucleotide added per enzyme molecule per second at various temperature.
Using this data, we determined kcat/Kn value at several temperatures and plotted the Arrhenius plot and the data agrees the Arrhenius plot properly.

## Slide 25
Experimental Estimation of
Enzyme Binding Rate Constant
Extension rate constant and Enzyme binding rate constants can be related as
P - The expected position of dissociation of the polymerase (expected stopping time) called the processivity
Marimuthu et al., Biophysical J (Under Review)
Notes: Extension reaction of single nucleotide insertion is represented by----
The rate equation can be derived ----
Innis et al determined the number of nucleotide added per enzyme molecule per second at various temperature.
Using this data, we determined kcat/Kn value at several temperatures and plotted the Arrhenius plot and the data agrees the Arrhenius plot properly.

## Slide 26
Summary of PCR Kinetic Model
Marimuthu et al., Biophysical J (Under Review)

## Slide 27
Outline
PCR Introduction and Unified Framework
Kinetic Model of PCR
Kinetic Analysis of Simplex PCR – Geometric Growth
Optimal Control of PCR
Conclusions.

## Slide 28
Overall Reaction Scheme of PCR and State Equations
.
.
.
If the length of the target is N, the total number of state equations are 4 N + 9 (N varies from 500 – 2000)
Stiff System of DE

## Slide 29
Transient Kinetics – Single Cycle (1st)
Length of the target – 1000 bp
If the annealing temperature is 40 deg C, the overall PCR is faster with nearly 100% efficiency.
Extension Reaction time – 30 seconds.
Annealing Reaction time – 45 seconds.
Extension temperature = 72 0 C
Enzyme Concentration = 10 nM.
Template Concentration = 10-14 M
Primer Concentration = 0.2 μM
Marimuthu et al., Biophysical J (Under Review)

## Slide 30
Transient Kinetics – Single Cycle (1st)
Maximum efficiency (based on these three sampling) of 70% is achieved at 35 0C
Same reaction conditions but different target sequence.
Sequence dependent Model is the key
Marimuthu et al., Biophysical J (Under Review)

## Slide 31
Geometric Growth of Target DNA
Shorter Reaction time
Longer
Reaction time

## Slide 32
Geometric Growth of Target DNA
Enzyme Concentration
is in Excess
Enzyme Concentration
is limited
Enzyme Concentration is constant throughout the PCR
Concentration of DNA increases when cycle no increases
Once single strands concentration exceeds the enzyme concentration, more enzyme is needed.
More enzyme can be provided when we recycle the enzyme.
SP is in Excess
Recycle this enzyme once it produce
some DNA so that it can react with all SP
Stage 1
Stage 2

## Slide 33
Multi Stage Approach (ith Cycle)
Two new types of PCR cycling strategies shown to improve the efficiency.
They can be further improved with the optimal control calculations.
Marimuthu and Chakrabarti (2014), Molecular Systems Biology, (Submitted)

## Slide 34
Minimizing Reaction time (Stage 1)
In stage 1, temperature profile is periodic – Pseudo first order reactions due to high enzyme and primer concentrations.
With fixed reaction time, find the cyclic efficiency that can reduce the overall reaction time – 100 % efficiency may not be desirable – Takes long time.
Solve the Following optimization problem

## Slide 35
Optimal Reaction time (Stage 1)
Marimuthu and Chakrabarti (2014), Molecular Systems Biology, (Submitted)
At each grid based sampling there exists an optimal cyclic efficiency and cycle time that can reduce the overall reaction time.

## Slide 36
Optimal Reaction time (Stage 1)
Marimuthu and Chakrabarti (2014), Molecular Systems Biology, (Submitted)

## Slide 37
Outline
PCR Introduction and Unified Framework
Kinetic Model of PCR
Kinetic Analysis of Simplex PCR
Optimal Control of PCR
Conclusions.

## Slide 38
Optimal Control Formulation
Optimal Condition
Pontryagin’s Maximum Principle -Two Point Boundary Value Problem

## Slide 39
Self Consistent Iterative Method(SCIM)

## Slide 40
Optimal Control
Optimal DNA concentration profile.
Initial Concentration of DNA is 10-14 M and Initial Concentration of Enzyme is 10 nM

## Slide 41
Time Optimal Control
Minimum time analysis using the optimal DNA concentration profile.

## Slide 42
Software Development
Sequence and Temperature Dependent Kinetic Model
Dynamic Optimization
Optimal Reaction Conditions

## Slide 43
Outline
PCR Introduction and Unified Framework
Kinetic Model of PCR
Kinetic Analysis of Simplex PCR
Optimal Control of PCR
Conclusions.

## Slide 44
Conclusions
Proposed a unified framework to design the new types of DNA amplification reactions.
We have developed the first sequence and temperature-dependent kinetic model for PCR reactions that is suitable for engineering control, validating this state space model through comparison to experimental data.
Our Systems Biology approach can be applied to various types of applications such as Polymerase Chain Reactions, Micro Array applications, Southern Blot, etc.

## Slide 45
Conclusions
Our kinetic model can be ‘easily’ extended to PCR with mismatches, Multiplex PCR, Cold PCR – Cancer Diagnosis.
New England Bio labs has shown interest to commercialize our work upon successful experimental validation.
Using the theory of Optimal Control, optimal temperature profile for a given PCR has been developed.
Using an approximate method to minimize the cycle time, the overall reaction time has been minimized.

## Slide 46
Contribution
Marimuthu, K and Chakrabarti, R - Sequence-dependent oligonuclotide hybridization kinetics : deterministic and stochastic theory. – Accepted to Journal of Chemical Physics.
Marimuthu, K , Jing, C and Chakrabarti, R - Sequence-dependent biophysical modeling of DNA amplification - Biophysical Journal (Under Review).
Marimuthu, K and Chakrabarti, R – Sequence-dependent theory of DNA amplification dynamics: toward optimally controlled DNA amplification – Molecular Systems Biology (Under Review).
Jing, C., Moorthy, S., Marimuthu, K., and Chakrabarti, R - Predictive kinetic modeling of DNA polymerases. To be Submitted.
Marimuthu, K and Chakrabarti, R – Optimally Controlled DNA amplification reaction – In Preparation.

## Slide 47
Thank You

## Slide 48
Thank You