## Slide 1
Aim: Standard curve with custom synthesized peptide in HDAC buffer with different concentrations of DHP2c.
Conditions
Peptide 3 (deacetylated FdL2 peptide) will be used as standard.
The standard will be run under 8 different solution conditions (0, 0.234675, 0.46875, 0.9375, 1.875, 3.75, 7.5, 15uM). This will cover the conditions used in endpoint and initial rate experiments.
FdL standard will be used as comparison.
Duplication will be performed.
Proposed Experiment PMC-XG4-2

## Slide 2
Avg | [Standard], uM | [DHP 2c], uM |  |  |  |  |  |  | 
 |  | 0 | 5 | 10 | 25 | 50 | 100 | 200 | 400
 | 15 | 2495.0 | 2517.5 | 2546.0 | 2552.5 | 2549.5 | 2524.0 | 2581.0 | 2444.5
 | 7.5 | 1181.5 | 1198.0 | 1223.5 | 1272.5 | 1363.5 | 1468.5 | 1729.5 | 1860.0
 | 3.75 | 532.5 | 539.5 | 583.5 | 677.5 | 763.5 | 986.0 | 1255.0 | 1485.0
 | 1.875 | 235.5 | 270.0 | 301.0 | 390.0 | 486.5 | 690.5 | 1017.0 | 1197.5
 | 0.9375 | 101.5 | 121.5 | 146.0 | 228.5 | 308.5 | 455.5 | 629.5 | 949.5
 | 0.46875 | 44.0 | 53.0 | 67.5 | 132.5 | 184.5 | 277.5 | 423.5 | 580.0
 | 0.234375 | 22.0 | 26.5 | 35.0 | 75.0 | 101.5 | 169.5 | 271.0 | 332.5
 | 0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Stdev | 15 | 66.5 | 54.4 | 55.2 | 44.5 | 129.4 | 49.5 | 39.6 | 12.0
 | 7.5 | 16.3 | 48.1 | 44.5 | 36.1 | 47.4 | 38.9 | 85.6 | 26.9
 | 3.75 | 20.5 | 4.9 | 21.9 | 27.6 | 24.7 | 11.3 | 41.0 | 2.8
 | 1.875 | 7.8 | 7.1 | 1.4 | 15.6 | 7.8 | 9.2 | 67.9 | 70.0
 | 0.9375 | 2.1 | 4.9 | 2.8 | 7.8 | 9.2 | 16.3 | 47.4 | 64.3
 | 0.46875 | 2.8 | 0.0 | 3.5 | 10.6 | 7.8 | 13.4 | 26.2 | 9.9
 | 0.234375 | 1.4 | 2.1 | 1.4 | 1.4 | 2.1 | 9.2 | 4.2 | 26.2
 | 0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
cv% | 15 | 2.7 | 2.2 | 2.2 | 1.7 | 5.1 | 2.0 | 1.5 | 0.5
 | 7.5 | 1.4 | 4.0 | 3.6 | 2.8 | 3.5 | 2.6 | 4.9 | 1.4
 | 3.75 | 3.9 | 0.9 | 3.8 | 4.1 | 3.2 | 1.1 | 3.3 | 0.2
 | 1.875 | 3.3 | 2.6 | 0.5 | 4.0 | 1.6 | 1.3 | 6.7 | 5.8
 | 0.9375 | 2.1 | 4.1 | 1.9 | 3.4 | 3.0 | 3.6 | 7.5 | 6.8
 | 0.46875 | 6.4 | 0.0 | 5.2 | 8.0 | 4.2 | 4.8 | 6.2 | 1.7
 | 0.234375 | 6.4 | 8.0 | 4.0 | 1.9 | 2.1 | 5.4 | 1.6 | 7.9
 | 0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0 | 0.0
Data Overview

## Slide 3
Chart: [Standard], uM
| 15 | 7.5 | 3.75 | 1.875 | 0.9375 | 0.46875 | 0.234375 | 0
 | 2495 | 1181.5 | 532.5 | 235.5 | 101.5 | 44 | 22 | 0
Chart: [Standard], uM
| 15 | 7.5 | 3.75 | 1.875 | 0.9375 | 0.46875 | 0.234375 | 0
 | 2517.5 | 1198 | 539.5 | 270 | 121.5 | 53 | 26.5 | 0
Chart: [Standard], uM
| 15 | 7.5 | 3.75 | 1.875 | 0.9375 | 0.46875 | 0.234375 | 0
 | 2546 | 1223.5 | 583.5 | 301 | 146 | 67.5 | 35 | 0
Chart: [Standard], uM
| 15 | 7.5 | 3.75 | 1.875 | 0.9375 | 0.46875 | 0.234375 | 0
 | 2552.5 | 1272.5 | 677.5 | 390 | 228.5 | 132.5 | 75 | 0
HDAC buffer
5uM DHP2c in HDAC buffer
25uM DHP2c in HDAC buffer
10uM DHP2c in HDAC buffer
Standard curves

## Slide 4
50uM DHP2c in HDAC buffer
100uM DHP2c in HDAC buffer
400uM DHP2c in HDAC buffer
200uM DHP2c in HDAC buffer
Chart: [Standard], uM
| 15 | 7.5 | 3.75 | 1.875 | 0.9375 | 0.46875 | 0.234375 | 0
 | 2524 | 1468.5 | 986 | 690.5 | 455.5 | 277.5 | 169.5 | 0
Chart: [Standard], uM
| 15 | 7.5 | 3.75 | 1.875 | 0.9375 | 0.46875 | 0.234375 | 0
 | 2581 | 1729.5 | 1255 | 1017 | 629.5 | 423.5 | 271 | 0
Chart: [Standard], uM
| 15 | 7.5 | 3.75 | 1.875 | 0.9375 | 0.46875 | 0.234375 | 0
 | 2444.5 | 1860 | 1485 | 1197.5 | 949.5 | 580 | 332.5 | 0
Chart: [Standard], uM
| 15 | 7.5 | 3.75 | 1.875 | 0.9375 | 0.46875 | 0.234375 | 0
 | 2549.5 | 1363.5 | 763.5 | 486.5 | 308.5 | 184.5 | 101.5 | 0

## Slide 5
Remarks:
The linearity of standard curves are fine for those in the presence of 0, 5, 10, 25, and 50 uM of DHP2c.
The linearity of standard curves become poor when the DHP2c concentration is reaching 100uM and above.
To get better understanding of what happened here, the following experiments are carried out.

## Slide 6
Chart: [DHP2c], uM
| 0 | 5 | 10 | 25 | 50 | 100 | 200 | 400
 | 0 | 243.3333 | 453.3333 | 1024 | 1704.3333 | 2617 | 3622 | 4129
[DHP2c], uM | Read 1 | Read 2 | Read 3 | Corrected Avg | Stdev | cv%
0 | 2 | 2 | 4 | 0 | 0 | 0
5 | 245 | 248 | 245 | 243 | 3 | 1.0
10 | 454 | 457 | 457 | 453 | 2 | 0.3
25 | 1020 | 1024 | 1036 | 1024 | 7 | 0.7
50 | 1686 | 1726 | 1709 | 1704 | 20 | 1.2
100 | 2625 | 2613 | 2621 | 2617 | 6 | 0.2
200 | 3628 | 3631 | 3615 | 3622 | 10 | 0.3
400 | 4129 | 4147 | 4119 | 4129 | 15 | 0.4
Exp. 1_ DHP2c background by TeCan
In the absence of developer, different concentrations of DHP2c solutions are prepared. The AFU of the solutions are measured.
Remarks:
DHP2c emits light at 460nm which overlap with AMC fluorophore.
The plot of AFU vs. [DHP2c] has poor linearity.
Question:
Why bad linearity?
Solution preparation problem?
Detection limitation of TeCan?
To answer above question, HPLC method is used for validation.

## Slide 7
Chart: [DHP2c], uM
| 0 | 5 | 10 | 25 | 50 | 100 | 200 | 400
3uM FdL2 peptide + 3mM NAD+ | 0 | 173463.5 | 339151 | 855677 | 1654969 | 3358791 | 6274492 | 12643795
250uM FdL2 peptide + 10uM NAD+ | 0 | 169916 | 343939 | 841813 | 1640106.5 | 3255982 | 6338760 | 12543590.5
250uM FdL2 peptide + 500uM NAD+ | 0 | 180112.5 | 352934 | 841539.5 | 1563192 | 3184453.5 | 6186886.5 | 11779519.5
DHP2c background – HPLC- peak area vs. [DHP2c]
Experimental conditions | r2 | Slope
3uM FdL2 peptide + 3mM NAD+ | 0.9996 | 31684
250uM FdL2 peptide + 10uM NAD+ | 0.9998 | 31504
250uM FdL2 peptide + 500uM NAD+ | 0.9989 | 29877
Avg | 31022 | 
Stdev | 995 | 
cv% | 3.2 | 
Looking through the DHP2c dose response HPLC data, it is found that under different experimental conditions (different combination of [FdL2 peptide] and [NAD+]), good linearity are spotted.
Remarks:
The plot of DHP2c Peak Area vs. [DHP2c] has good linearity under different experimental conditions (different combination of [FdL2 peptide] and [NAD+]),
This indicates that DHP2c solution preparation is fine.

## Slide 8
For standard curve, does standard (deacetylated peptide_p53-QPKK-AMC) itself contribute total AFU?

## Slide 9
For standard curve, does standard (p53-QPKK-AMC) contribute total AFU?
[Standard], uM | Enzo Standard |  |  |  | Synthesized Standard |  |  | 
 | No Developer |  | Yes Developer |  | No Developer |  | Yes Developer | 
 | Run1 | Run2 | Run1 | Run2 | Run1 | Run2 | Run1 | Run2
0 | 6 | 4 | 17 | 15 | 5 | 4 | 16 | 17
0.234375 | 6 | 5 | 135 | 135 | 3 | 6 | 59 | 62
0.46875 | 5 | 6 | 241 | 243 | 2 | 4 | 98 | 102
0.9375 | 6 | 7 | 455 | 440 | 5 | 3 | 174 | 180
1.875 | 9 | 8 | 798 | 801 | 3 | 5 | 293 | 320
3.75 | 12 | 14 | 1437 | 1422 | 7 | 5 | 577 | 582
7.5 | 21 | 24 | 2547 | 2523 | 9 | 11 | 1060 | 1109
15 | 38 | 38 | 4247 | 3347 | 14 | 14 | 1840 | 1828
Remarks: No. Standard samples itself do not contribute in total AFU!
Both Enzo and synthesized FdL2 peptide samples do not contain free AMC.
  For sample solutions without the addition of developer, the AFU readout are close to zero. This indicated no free AMC was in the sample.
  There is a little signal, <=38 for Enzo sample, and <=14 for synthesized sample, which can be treated as background.
  For sample solutions with the addition of developer, the linear correlation between AFU vs. [standard] is detected. This indicates that trypsin cleavage reaction proceed well.
Enzo standard provides much stronger AFU readout (slope =299.2 and 126.71 respectively) comparing to synthesized one.
The linearity of standard curve from synthesized peptide is better than Enzo one’s.
Chart: [Standard], uM
| 0 | 0.234375 | 0.46875 | 0.9375 | 1.875 | 3.75 | 7.5 | 15
Enzo Standard | 0 | 118 | 224 | 438 | 781 | 1420 | 2530 | 4230
Synthesized standard | 0 | 43 | 82 | 158 | 277 | 561 | 1044 | 1824

## Slide 10
Remarks
The above analysis indicates that in the absence of DHP2c or lower concentrations of DHP2c (<=50uM), the standard curves can be used for quantification.
However, in the presence of higher concentrations of DHP2c (>=100uM), standard curve can not be used for data analysis.
The presence of higher concentrations of DHP2c interfere the total AFU readout and over write the signals generated by free AMC cleaved from deacetylated peptide (product). The misinterpretation of the AFU data direct the false positive results by using FdL assay.
FdL assay use free AMC, generated from deacetylated peptide (product) , as readout. In principle, the AFU from TeCan represents the amount of deacetylated peptide formed under certain condition such as [NAD+], [FdL2 peptide substrate], reaction time, and modulator effect. What else can make contribution to the total AFU?
Does FdL2 peptide (p53-QPKKAC-AMC) itself contribute total AFU?

## Slide 11
Chart: [FdL2 peptide], uM
| 0 | 1.953125 | 3.9062499999999996 | 7.8124999999999991 | 15.625 | 31.25 | 62.5 | 125 | 250 | 500
Enzo FdL2 peptide_No Developer | 0 | 5 | 10.5 | 34 | 44.5 | 90.5 | 182 | 328 | 666 | 1180.5
Enzo FdL2 peptide_1X Developer | 0 | 3.5 | 7.5 | 18 | 36.5 | 74 | 150 | 301 | 576.5 | 1040
Synthesized FdL2 peptide_ No developer | 0 | 2.5 | 3 | 5.5 | 10 | 21.5 | 42.5 | 84 | 164.5 | 321
Synthesized FdL2 peptide_ 1 x developer | 0 | 1.5 | 1.5 | 3.5 | 5.5 | 13.5 | 26 | 57 | 115 | 233
Does FdL2 peptide (p53-QPKKAC-AMC) itself contribute total AFU?
[ ], uM | Enzo FdL2 peptide |  | Synthesized FdL2 peptide | 
 | No Developer | Yes Developer | No Developer | Yes Developer
0 | 0 | 0 | 0 | 0
1.953125 | 5 | 4 | 3 | 2
3.90625 | 11 | 8 | 3 | 2
7.8125 | 34 | 18 | 6 | 4
15.625 | 45 | 37 | 10 | 6
31.25 | 91 | 74 | 22 | 14
62.5 | 182 | 150 | 43 | 26
125 | 328 | 301 | 84 | 57
250 | 666 | 577 | 165 | 115
500 | 1181 | 1040 | 321 | 233
Remarks: Yes. FdL2 peptide itself contributes in total AFU!
Both Enzo and synthesized FdL2 peptide samples contain free AMC, which counted as background.
  No developer solutions only contain FdL2 peptide (p53-QPKKAc-AMC). If there is no free AMC, the AFU readout should close to zero.
  In no developer solutions, the AFU readout increases along [FdL2 peptide] increasing. A good linear correlations are found, which indicates free AMC is FdL2 peptide dose response.
  The addition of developer does not bring up the AFU readout further. This indicates there is no deacetylated peptide impurity (p53-QPKK-AMC) in the sample.
Enzo FdL2 peptide provide much bigger background.
This type of background can be eliminated by having a control sample for background subtraction.

## Slide 12
Proposed Experiment PMC-XG4-3
Aim: DHP1c does response experiment-FdL assay on TeCan
Condition 1: [FdL2 peptide] = 3uM; [NAD+]=3000uM
Condition 2: [FdL2 peptide] = 250 uM; [NAD+] = 10uM.
Condition 3: [FdL2 peptide] = 250 uM; [NAD+] = 500uM
[DHP2c]=0, 5, 10, 25, 50, 100, 200, 400uM.
[Enzo/In-house SIRT3] = 10 U
Time points = 0, 60 min

## Slide 13
[DHP2], uM | 0min | 60min | DAFU
0 | 19 | 27 | 8
5 | 110 | 109 | -1
10 | 197 | 190 | -7
25 | 433 | 421 | -12
50 | 740 | 673 | -67
100 | 1253 | 1171 | -82
200 | 1996 | 1902 | -94
400 | 2707 | 2535 | -172
Condition I: 3000uM NAD + 3 uM FdL2 peptide
Chart: [DHP2c], uM
| 0 | 5 | 10 | 25 | 50 | 100 | 200 | 400
 | 8 | -1 | -7 | -12 | -67 | -82 | -94 | -172

## Slide 14
[DHP2], uM | 0min | 60min | DAFU
0 | 222 | 268 | 46
5 | 302 | 339 | 37
10 | 373 | 407 | 34
25 | 643 | 671 | 28
50 | 994 | 1016 | 22
100 | 1512 | 1521 | 9
200 | 2339 | 2294 | -45
400 | 3021 | 2899 | -122
Condition II: 10uM NAD + 250 uM FdL2 peptide
Chart: [DHP2c], uM
| 0 | 5 | 10 | 25 | 50 | 100 | 200 | 400
 | 46 | 37 | 34 | 28 | 22 | 9 | -45 | -122

## Slide 15
[DHP2], uM | 0min | 60min | DAFU | % Activity
0 | 220 | 1764 | 1544 | 100.0
5 | 299 | 1656 | 1357 | 87.9
10 | 381 | 1725 | 1344 | 87.0
25 | 651 | 1972 | 1321 | 85.6
50 | 987 | 2102 | 1115 | 72.2
100 | 1503 | 2323 | 820 | 53.1
200 | 2308 | 2920 | 612 | 39.6
400 | 3029 | 3305 | 276 | 17.9
Condition III: 500uM NAD + 250 uM FdL2 peptide
Chart: [DHP2c], uM
| 0 | 5 | 10 | 25 | 50 | 100 | 200 | 400
 | 1544 | 1357 | 1344 | 1321 | 1115 | 820 | 612 | 276
Chart: [DHP2c], uM
| 0 | 5 | 10 | 25 | 50 | 100 | 200 | 400
 | 100 | 87.8886 | 87.0466 | 85.557 | 72.215 | 53.1088 | 39.6373 | 17.8756

## Slide 16
Remarks
Condition I and II: negative number are obtained.
Condition III: % Activity decreased as increasing DHP2c concentration.
As analysis made on PMC-XG-4-2, the overall AFU readout is the competition among (1) free AMC generated from product, (2) DHP2c background, (3) FdL2 peptide itself. Under condition I and II, the amount of product (deacetylated FdL peptide) are low. The AFU contributed by free AMC is low can not overcome DHP 2c background. Therefore the Delta AFU become more and more negative along DHP2c concentration increasing.
Under condition III, though AFU from free AMC is big enough, as mentioned in PMC ST-4-2, the DHP2c AFU vs. [DHP2c] plot is not linear. It indicated at higher [DHP2c], the AFU readout is less than what it suppose to be. Therefore, we saw the decrease of % Activity.
To conclude:
The presence of higher concentrations of DHP2c interfere the total AFU readout and over write the signals generated by free AMC cleaved from deacetylated peptide (product). The misinterpretation of the AFU data direct the false positive results by using FdL assay.