## Slide 1: Materials
DNA Template and Primer: The template for the polymerase assay is an 80-mer single stranded DNA, TAT2, custom synthesized by Sigma Custom Oligos. A 17-mer primer TAP1, complementary to the 17 bases at the 3’ end of TAT2 was also custom synthesized by Sigma Custom Oligos. (see table 1 for GC content and calculated Tm).
Reaction Components: Native Taq Polymerase (with its buffer and MgCl2) is obtained from Life Technologies, dNTP mix from New England Biolabs, Quant-iT PicoGreen ds DNA Reagent from Molecular Probes.
Instruments: The incubation for the activity assays are carried out in the BioRad CFX96 PCR machine (software: CFX Manager ver 1.6.541.1028). PicoGreen fluorescence is measured in the Lab Systems Fluoroskan Ascent Fluorescence 96/384 Well Plate Reader using a PCR plate adapter (Excitation 485nm; Emission 520nm).
Software: Calculation of Tms of synthetic oligomers was done using Sigma DNA Calculator, http://www.sigma-genosys.com/calc/DNACalc.asp. Analysis of secondary structures and of primer-dimer formation was done according to Oligo Analyzer from IDT: http://biotools.idtdna.com/analyzer/applications/oligoanalyzer/ . GraphPad Prism was used for all curve fittings.
Table 1 : Oligos used in the study |  |  |  | 
Oligo (length) | Sequence | % GC | Tm | Description
TAT2 (80 bases) | 5’- ACA CGT TAG GAA GAT GGA ATT GAT TGG ATC GAA GGA AAT AAA AGA AAT TAA GGC AAT GGT CTC CCG TCG GCG GCG CGA GC-3’ | 47.5 | 92oC | Template for Taq polymerase extension
TAT1 (17 bases) | 5’-GCT CGC GCC GCC GAC GG-3’ | 88 | 80oC | Primer for TAT2

## Slide 2: Method 1
Preparation of Template-Primer Mix (see Table 2 for details) :
The single stranded 80-mer template, TAT2 and it 17-mer primer TAP1 were mixed such that the primer was present in a 7 molar excess (this is the molar ratio used in the previous study) in 1X Taq reaction buffer (20 mM Tris-HCl, 50 mM KCl) containing 2mM MgCl2.
The holding and cooling steps for annealing were as follows (as used in the previous study): hold at 95oC for 1.5 minute, cool to 75oC over 30 minutes, hold at 75oC for 5 minutes, cool to 70oC over 9 minutes, hold at 70oC for 5 minutes, cool to 45oC over 45 minutes and then to room temperature on the bench. (The annealed primer-template complex mix is stored at room temperature for the duration of the assay for up to 24hrs. It is neither chilled nor frozen).
Table 2: Composition of the Template-Primer mix |  | 
Initial Conc | Reaction Component | Final Conc
 | Template (TAT2) | 20nM
 | Primer (TAP1) | 140nM
10X | Taq Polymerase Buffer | 1X
50mM | MgCl2 | 2mM

## Slide 3: Method 2
Set up of the Reaction (see Table 3 for details):
In this initial trial of the new protocol, one complete time course at 70oC was performed for two enzyme concentrations (0.36nM used previously and 0.02nM which achieves the template: enzyme ration of 1000). Each time point had 2 replicates each for reactions with the 5min equilibration and reactions with no equilibration. The template-primer mix was made/ annealed as a single batch for this entire set.
The template-primer mix was split into 11parts, one for each assay time point (see table) and one for a no-Taq control. Taq Polymerase (appropriately diluted in the dilution buffer to achieve the final concentration stated in the table in each 20ul reaction) was added to the test fractions and water was added to the no-Taq control fraction.
For each time point, two aliquots of the reaction were incubated at 70oC in the CFX96 (PCR machine) for 5mins (for equilibration of the Taq polymerase with the primer-template complex).
After equilibration, the polymerase reaction was initiated by addition of dNTPs (see table for concentration). Simultaneously, two reactions were initiated without equilibration.
At the end of the incubation the reaction was immediately chilled to 0oC and EDTA was added to a final conc of 20mM.
Table 3: Assay Variables | 
Temperature | 70oC (in the initial trial)
Time points | 10secs, 20secs, 30secs, 40secs, 50secs, 1min, 1.5mins, 2mins, 5mins, 10mins
Enzyme Concentration | 0.02nM vs 0.36nM
dNTP Concentration | 200mM (for the initial trial)
Replicates | 2
Reaction Volume | 20ul

## Slide 4: Method 3
Quantitation:
  80ul of Picogreen reagent freshly diluted 178-fold in 1X TE was added to each reaction. The reaction was incubated in the dark for 5min at room temperature and fluorescence is measured in the Fluoroskan with excitation at 485nm and emission at 520nm.
Plots:
  The measured RFU was plotted against time. The curves were fitted using the equation for one-phase association kinetics. The initial reaction rate (del RFU/sec) was calculated using the corrected RFU values from the fitted curve.

## Slide 5: Taq Polymerase activity measured at 70oC over 10mins 20nM Template and 0.36nM Taq in a 20ul reaction: Comparison of 5min equilibration of Taq Polymerase with the primed template at 70oC vs no equilibration
0.36nM Taq is the concentration used in the previous study. Equlibration with Taq polymerase at the assay temperature has not been done previously. Since activity is very high, even at the earliest time point of the assay (10secs) activity appears to have plateaued (see scale up of the first 1 or first 2mins on the right). Early time point RFUs are not accurate and curve fit is poor. (For this template and enzyme concentration, lower assay temperatures (lower measurable activity) will give more accurate RFU values.

## Slide 6: Taq Polymerase activity measured at 70oC over 10mins 20nM Template and 0.02nM Taq in a 20ul reaction: Comparison of 5min equilibration of Taq Polymerase with the primed template at 70oC vs no equilibration
0.02nM is the recommended concentration of Taq Polymerase to give a primed-template:Taq ratio of 1000:1. Because of this low concentration of Taq, even the measurements at early time point of the assay are closer to the fitted curve (see scale up of the first 1 or first 2mins on the right). Also, even at 10mins, the activity does not seem to have plateaued. (For this template and enzyme concentration, low assay temperatures (eg., 45-50oC as have been used previously) may not give measurable activity. Assay may need to include time points greater than 10mins.

## Slide 7: Taq Polymerase activity measured at 70oC over 10mins 5min equilibration of Taq Polymerase with the primed template at 70oC 20nM Template with 0.36nM vs 0.02nM Taq in a 20ul reaction
Activity of 0.02nM Taq (the recommended concentration of Taq Polymerase to give a primed-template:Taq ratio of 1000:1) is compared with 0.36nM Taq (as used previously) at 70oC. These reactions had a pre-incubation at 70oC for equilibration of Taq polymerase with the primed-template.

## Slide 8: Taq Polymerase activity measured at 70oC over 10mins No equilibration of Taq Polymerase with the primed template at 70oC 20nM Template with 0.36nM/ 0.02nM Taq in a 20ul reaction
Activity of 0.02nM Taq (the recommended concentration of Taq Polymerase to give a primed-template:Taq ratio of 1000:1) is compared with 0.36nM Taq (as used previously) at 70oC. These reactions did not have a pre-incubation at 70oC for equilibration of Taq polymerase with the primed-template.

## Slide 9: Summary
Since the recommended enzyme concentration is very low, the trial activity assay was carried out at 70oC where previously the maximum activity has been noted.
  Initial reaction rate is quite low
  Early time point measurement seems reliable
  Even at 10mins the enzyme may not have saturated
  The initial reaction rate appears to be
    +eqbrn: 2.94 x 10-13 mols dNTP incorporated/sec by 0.01U Taq
    - eqbrn: 2.08 x 10-13 mols dNTP incorporated/sec by 0.01U Taq
  This difference in reaction rate may not be significant for the following reasons:
    The test condition has been assayed only once (reproducibility has not been determined)
    The equilibration time has not been varied (5min vs 10mins, 15mins, 20mins etc).
Next proposed experiments:
  Vary equilibration time (essential to understand if 5mins is enough)
  At the defined equilibration time, vary [dNTP] concentration (necessary to calculate the kinetic parameters)
  If required vary assay temperature (65oC, 75oC) (Optional)
  Replication of assays to test for reliability and reproducibility (Essential)
See table in the following page

## Slide 10: Estimate of time for completion
Steps | Primed-template: Taq | dNTP concentration | Equilibration Time | Assay temperature | No. of Assays* | No. of weeks required
Standardisation of Equilibration time | 20nM:0.02nM | 200mM | 0, 5, 10, 20 mins | 70oC | 4 | 0.8
Variation of [dNTP] | 20nM:0.02nM | 0.2X (ie 50mM), 1X (ie 200mM), 5X (ie 1000mM) | Determined from above | 70oC | 3** | 0.5
Variation of assay temperatues | 20nM:0.02nM | Determined from above | Determined from above | 65oC, 70oC, 75oC | 3 (at each dNTP conc)*** | 2.5
Replication | 20nM:0.02nM | Determined from above | Determined from above | 65oC, 70oC, 75oC | 3 (at each dNTP conc) | 2.5
*: Each assay has 12 time points; involves ~3hrs for setting up the extension reactions and ~30mins for quantitation; and also involves 1 day’s prior work to prepare buffers etc and make and anneal the template-primer mix and ~1 days work afterword to plot the data on Prism and perform necessary calculations. |  |  |  |  |  | 
**: Three [dNTP] concentrations will not be enough to plot the Michaelis-Menten curves. But this would be an initial check to see that the range works. |  |  |  |  |  | 
***: Varying the assay temp is optional, however it WILL show that the experimental protocol is stable and robust. With the low concentration of Taq in these set of assays, temps lower than 65 may not give measurable activity. |  |  |  |  |  | 

## Slide 11: Update 042513
Recommendation based on the results of the extension assay at 70oC:
  Increase equilibration time to 30mins keeping all else same.
Given that melting temperature of the primer is 80oC, this recommendation was revisited (for an oligo with a Tm of 80oC, melting could already have started at 70oC; thus prolonging equilibration time leads to conflict between DNA melting and enzyme binding.)
Alternative recommendation was to decrease the assay temperature (if melting is prevented, the effect of (prolonged) equilibration may be seen).
  Assay at 60oC, compare 5min equilibration with no equilibration
The following slide represents the results from the extension assay at 60oC.

## Slide 12: Taq Polymerase activity measured at 60oC over 10mins 20nM Template and 0.02nM Taq in a 20ul reaction: Comparison of 5min equilibration of Taq Polymerase with the primed template at 60oC vs no equilibration
Activity of 0.02nM Taq (the recommended concentration of Taq Polymerase to give a primed-template:Taq ratio of 1000:1) at 60oC. Reactions with a pre-incubation at 60oC/ 5mins for equilibration of Taq polymerase with the primed-template are compared with reactions with no pre-incubation. Reactions with equilibration show lower initial activity rates than reactions without equilibration.
Early time point (10-50secs) did not appear accurate and needed to be eliminated for optimum curve fitting.

## Slide 13: Update 050213
It was decided that 5min equilibration is short and given current experimental practicalities (and/or limitations), comparison of 5min equilibration with no equilibration is not accurate. Therefore decided to increase equilibration to 30mins.
See following slide (14) for results of the extension assay at 60oC comparing 30min equilibration with no equilibration.
  Slides 15-16 compare the two 60oC extension assays (5min/ no equilibration and 30min/ no equilibration), by plotting the -eqbrn curves together and the +eqbrn curves together. Since these respective values are close, the replicate means of –eqbrn (5min eqbrn and 30min eqbrn expts) and replicate means of +eqbrn (5min eqbrn and 30min eqbrn expts) were taken as individual data points and a single plot for - eqbrn and +eqbrn created (slide 17).
In all conditions tested so far (including results on slide 14), reactions without equilibration show higher initial activity.
  Should we conclude that equilibration is extremely fast and eliminate this pre-incubation step from the assay?
NOTE: Compared to previously conducted assays,
  there is a slight difference in the actual handling of reactions in the current assay set, since + and – eqbrn reactions are being treated simultaneously. This could lead to differences. Can be controlled for by
    setting up +eqbrn and –eqbrn reactions separately.
  the assays of the current set appear to have a slightly higher background (0min –taq RFU), which needs to be resolved.
    each time point can have its own no taq ctrl, this should ensure tighter control of background RFU.
  early time points of the assays of the current set are not as accurate as seen before and need to be eliminated during curve fitting
    could be explained by the lower enzyme concentration

## Slide 14: Taq Polymerase activity measured at 60oC over 10mins 20nM Template and 0.02nM Taq in a 20ul reaction: Comparison of 30min equilibration of Taq Polymerase with the primed template at 60oC with no equilibration
Activity of 0.02nM Taq (the recommended concentration of Taq Polymerase to give a primed-template:Taq ratio of 1000:1) at 60oC. Reactions with a pre-incubation at 60oC/ 30mins for equilibration of Taq polymerase with the primed-template are compared with reactions with no pre-incubation. This was done because comparison of 5min eqbrn with no eqbrn appeared error-prone.
No equilibration reactions again appear to have higher initial reaction rate than reactions equilibrated for 30mins.

## Slide 15: Taq Polymerase Activity at 60oC: No equilibration reactions from slides 12 and 14 plotted together Show same initial rate of activity
Curves do not superimpose on each other, however, calculated initial reaction rates for both curves are same.
Bear in mind that these are (so far single-instance) experiments from different days. Also, given the small range, differences appear magnified. Please note RFU values (these are means of the 3 replicates set up in each experiment).
These curves were plotted together to understand day-to-day variations for the same set of test conditions.
Mins | Mean (-30min eqbrn rpt) | Mean (-5min eqbrn)
10.00 | 1.81 | 1.72
5.00 | 1.89 | 1.51
2.00 | 1.47 | 1.34
1.00 | 1.41 | 1.35
0.83 | 1.35 | 1.19
0.66 |  | 
0.50 |  | 
0.33 |  | 
0.00 | 1.14 | 0.91

## Slide 16: Taq Polymerase Activity at 60oC: Reactions with equilibration (5min-slide 12 and 30min-slide 14) plotted together Equilibration for 5min/ 30min results in the same level of activity
Mins | Mean (+30min eqbrn rpt) | Mean ( +5min eqbrn rpt)
10.00 | 1.56 | 1.71
5.00 | 1.63 | 1.50
2.00 | 1.25 | 1.23
1.00 |  | 1.18
0.83 | 1.21 | 1.20
0.66 |  | 
0.50 |  | 
0.33 | 1.21 | 1.26
0.00 | 1.07 | 0.78
Curves almost superimpose on each other, thus 5/ 30min eqbrn does not seem to affect initial rate of activity. Bear in mind, given the small range, differences appear magnified. Please note RFU values (these are means of the 3 replicates set up in each experiment).

## Slide 17: Taq Polymerase Activity at 60oC: Summary of +equilibration and –equilibration assays
Since activities for +eqbrn and - eqbrn states in the two 60oC expts were similar, mean RFUs of the two experiments have been plotted. As expected, no eqbrn rate is higher than +eqbrn. Although curve-fitting is tolerable (R square= ~0.8), the net RFU change is too small for this activity assay to be reliable.

## Slide 18: Comparisons of previous extension assays (0.36nM Taq no equilibration) with the current assay set (0.02nM Taq no equilibration reactions)
Time | NMP-No solvt expt Oct'12 60oC |  |  |  | No solvt expt Mar'12 65oC |  |  |  | No solvt expt for eqbrn Apr'13 60oC |  |  | 
 | Rep 1 | Rep 2 | Rep 3 | Mean | Rep 1 | Rep 2 | Rep 3 | Mean | Rep 1 | Rep 2 | Rep 3 | Mean
10.0 | 2.98 | 2.50 | 2.88 | 2.79 | 2.82 | 3.28 | 3.42 | 3.17 | 1.81 | 1.94 | 1.72 | 1.82
5.0 | 2.75 | 2.42 | 2.77 | 2.65 | 3.66 | 4.18 | 3.58 | 3.81 | 1.89 | 1.79 | 1.51 | 1.73
2.0 | 1.83 | 1.72 | 1.90 | 1.82 | 2.88 | 2.74 | 3.17 | 2.93 | 1.47 | 1.46 | 1.34 | 1.42
1.5 | 1.66 | 1.56 | 1.54 | 1.59 | 2.44 | 2.74 | 2.90 | 2.69 |  |  |  | 
1.0 | 1.55 | 1.33 | 1.55 | 1.48 | 2.45 | 2.22 | 2.32 | 2.33 | 1.41 | 1.43 | 1.35 | 1.40
0.8 |  |  |  |  |  |  |  |  | 1.35 |  | 1.19 | 1.27
0.8 | 1.24 | 1.22 | 1.12 | 1.20 | 1.85 | 2.11 | 1.88 | 1.94 |  |  |  | 
0.7 |  |  |  |  |  |  |  |  |  |  |  | 
0.5 | 1.19 | 1.01 | 1.03 | 1.08 | 1.54 | 1.61 | 1.13 | 1.43 |  |  |  | 
0.3 |  |  |  |  |  |  |  |  |  | 1.33 |  | 1.33
0.3 | 1.18 | 1.19 | 1.16 | 1.18 | 1.33 | 1.37 | 1.38 | 1.36 |  |  |  | 
0.0 | 0.69 | 0.57 |  | 0.63 | 0.62 | 0.70 | 0.67 | 0.66 | 1.14 | 1.29 | 0.91 | 1.11
The net gain is RFU is much smaller in the current assay set. (This also magnifies the variation in replicates, particularly when viewed individually rather than in comparison with other test conditions.)
As can be seen here the slightly higher background RFU could be tolerated (or may not be significant) if the net RFU gain was higher.

## Slide 19: Update 050713
Based on recommendations of 050213:
+equilibration and –equilibration reactions were set up separately but from the same annealed template-primer master mix.
Each time point had its own –taq control
30min equilibartion and activity at 60oC was performed.
Since the net gain in RFU was very small with 20nM template:0.02nM Taq (as used so far), for the following assays, template has been increased to 200nM and Taq has been brought back to 0.36nM (template:taq ratio 555.55)
See slides 20, 21 for raw data and slide 22 for processed data
Although these reactions cannot be compared to previous assays of the current series (due to altered template:taq ratios), equilibrated reactions still show lower initial activity than non-equilibrated reactions.
It is not possible to compare the non-equilibrated reactions in this assy with older assay results (March 2012 200nM/ 100ng template) because the previous assays were quantitated as 10ul aliquots of the 20ul reaction (and) without a plate adapter. However, net gain in RFU values seems to be in the same range.

## Slide 20: Taq Polymerase activity measured at 60oC over 10mins 200nM Template and 0.36nM Taq in a 20ul reaction: These reactions without equilibration. Each time point had a corresponding no taq control reaction The individual RFUs of +taq and -taq reactions were plotted and mean and SE calculated
A | B | C | D | E | F | G | H | I | J | K | L | M
 | + taq |  |  |  | - taq |  |  |  | RFU+taq - RFU-taq |  | RFU+taq -mean RFU-taq | 
Mins | Rep 1 | Rep 2 | Rep 3 | mean | Rep 1 | Rep 2 | Rep 3 | mean |  | 0 crrctd |  | 0 crrctd
10.00 | 10.09 | 11.79 | 9.675 | 10.52 | 6.118 | 5.99 | 7.277 | 6.46 | 4.06 | 2.03 | 3.8620 | 1.45
5.00 | 11.06 | 11.51 | 11.3 | 11.29 | 7.152 | 6.766 | 7.728 | 7.22 | 4.07 | 2.05 | 4.6337 | 2.22
2.00 | 8.271 | 8.25 | 7.612 | 8.04 | 5.905 | 6.41 | 5.936 | 6.08 | 1.96 | -0.06 | 1.3880 | -1.02
1.00 | 9.124 | 9.109 | 9.076 | 9.10 | 6.931 | 6.577 | 6.611 | 6.71 | 2.40 | 0.37 | 2.4467 | 0.03
0.83 | 9.074 | 8.763 | 8.622 | 8.82 | 6.822 | 6.305 | 6.087 | 6.40 | 2.42 | 0.39 | 2.1633 | -0.25
0.66 | 8.833 | 8.82 | 8.393 | 8.68 | 6.861 | 6.517 | 6.77 | 6.72 | 1.97 | -0.06 | 2.0257 | -0.39
0.50 | 9.084 | 9.233 | 8.108 | 8.81 | 6.631 | 6.632 | 6.483 | 6.58 | 2.23 | 0.20 | 2.1520 | -0.26
0.33 | 10.03 | 8.223 | 8.286 | 8.85 | 6.593 | 6.786 | 6.701 | 6.69 | 2.15 | 0.13 | 2.1900 | -0.22
0.00 | 9.098 | 9.072 | 9.036 | 9.07 | 8.04 | 7.298 | 6.79 | 7.04 | 2.02 | 0.00 | 2.4123 | 0.00
 |  |  |  |  | mean -taq value (0-10mins) |  |  | 6.66 |  |  |  | 
 |  |  |  |  |  | SD(0-10mins) |  | 0.33632 |  |  |  | 

## Slide 21: Taq Polymerase activity measured at 60oC over 10mins 200nM Template and 0.36nM Taq in a 20ul reaction: These reactions with 30min equilibration. Each time point had a corresponding no taq control reaction The individual RFUs of +taq and -taq reactions were plotted. mean and calculated
A | B | C | D | E | F |  | G |  | H |  | I | J | K | L | M
 | + taq |  |  |  | - taq |  |  |  |  |  |  | RFU+taq - RFU-taq |  | RFU+taq -mean RFU-taq | 
Mins | Rep 1 | Rep 2 | Rep 3 | mean | Rep 1 | Rep 2 |  | Rep 3 |  | mean |  |  | 0 crrctd |  | 0 crrctd
10.00 | 9.654 | 11.33 | 9.727 | 9.69 | 6.502 | 5.68 |  | 7.979 |  | 6.72 |  | 2.49 | 1.71 | 2.6833 | 2.25
5.00 | 9.138 | 10.64 | 9.656 | 9.40 | 7.487 | 7.924 |  | 7.806 |  | 7.74 |  | 2.20 | 1.41 | 2.3898 | 1.96
2.00 | 7.537 | 9.651 | 8.471 | 9.06 | 7.956 | 6.846 |  | 7.217 |  | 7.34 |  | 1.72 | 0.94 | 2.0538 | 1.63
1.00 | 9.409 | 8.534 | 8.564 | 8.55 | 5.864 | 7.28 |  | 6.959 |  | 6.70 |  | 1.85 | 1.07 | 1.5418 | 1.11
0.83 | 9.283 | 9.166 | 8.622 | 9.02 | 6.728 | 7.635 |  | 7.526 |  | 7.30 |  | 1.73 | 0.94 | 2.0164 | 1.59
0.66 | 8.471 | 8.623 | 8.313 | 8.47 | 7.203 | 6.489 |  | 6.268 |  | 6.65 |  | 1.82 | 1.03 | 1.4618 | 1.03
0.50 | 8.208 | 8.987 | 8.582 | 8.40 | 6.853 | 7.193 |  | 7.333 |  | 7.13 |  | 1.27 | 0.49 | 1.3878 | 0.96
0.33 | 8.121 | 8.185 | 8.33 | 8.21 | 7.124 | 7.387 |  | 5.995 |  | 6.84 |  | 1.38 | 0.59 | 1.2048 | 0.78
0.00 | 7.084 | 7.651 | 7.573 | 7.44 | 6.749 | 6.848 |  | 6.364 |  | 6.65 |  | 0.78 | 0.00 | 0.4288 | 0.00
 |  |  |  |  | Mean –taq value (0-10mins) |  |  |  |  | 7.01 |  |  |  |  | 
 |  |  |  |  |  | SD(0-10mins) |  |  |  | 0.387242 |  |  |  |  | 

## Slide 22: Each time point has a corresponding no taq control reaction RFU+taq - RFU -taq = DRFU The zero corrected DRFUs were plotted to determine the net gain in RFU in 10mins.
The first 2 data points of the fitted curves to compare 0min values and calculate rates
Chart: Zero corrected DRFU vs time for Taq Polymerase Activity at 60oC: Comparison of reactions with and without 30min equilibration
-eqbrn |  |  |  |  | +eqbrn |  |  |  | 
Mins | +taq | -taq | RFU+taq - RFU-taq = DRFU | zero corrected DRFU | Mins | +taq | -taq | RFU+taq - RFU-taq = DRFU | zero corrected DRFU
0.0000 | 8.4074 | 7.0331 | 1.3742 | 0.0000 | 0.0000 | 7.5422 | 6.6607 | 0.8815 | 0.0000
0.0671 | 8.4698 | 6.9466 | 1.5232 | 0.1489 | 0.0671 | 7.6942 | 6.7010 | 0.9931 | 0.1116
Plot I Plot II
The fitted curves (from slide 20, 21) were used to calculate the DRFU for each time point for both sets of taq reactions (with and without equilibration). These values were zero corrected and plotted together to calculate initial rates of taq activity (Plot I). The fitted curves (from slides 20, 21) which were used are plotted together (Plot II) for purposes of comparison.
Chart: Prism-corrected Time Courses for +Taq and -Taq reactions before determining DRFU vs time plots for 30min eqbrn vs no eqbrn