## Slide 1
Trial purification of full-length Sirt3 (102-399) from AE (DE3) cells, using the AKTA pure FPLC system

## Slide 2: FPLC method
Trial run done using 1 ml His-Trap column and frozen Sirt3-AE cells from 200 ml culture.
Method progress monitored by measuring absorbance at 280 nm.
Column equilibrated with 20 cv Equilibration buffer (LEW 1X with 20 mM imidazole) at 1 ml/min.
~5ml sample loaded at 0.5 ml/min.
Column washed with 20 cv Equilibration buffer (20 mM imidazole) at 1 ml/min (Wash step 1).
Column washed with 20 cv Wash 1 buffer (75 mM imidazole) at 1 ml/min (Wash step 2).
Column washed with 10 cv Wash 2 buffer (2 M urea) at 1 ml/min (Wash step 3).
Column washed with 20 cv Wash 1 buffer (75 mM imidazole) at 1 ml/min (Wash step 4).
Sirt3 eluted with Elution buffer (300 mM imidazole) as 300 ul fractions.

## Slide 3
Full chromatogram of run
Equilibration
Sample loading
Wash step 1
Wash step 2
Wash step 3
Wash step 4
Elutions

## Slide 4
Elution peak
Most concentrated elutions

## Slide 5
FT
Elutions
9
10
11
12
Sirt3
SDS-PAGE analysis of flowthrough and elutions
FT = Flowthrough
Elutions 9-12 correspond to the most concentrated fractions in the elution peak.
Purity (> 85%), similar to that obtained from manual purification.
Next steps:
Scale up method using 5 ml column; analyze results.
Based on above results, scale up to 20 ml column for bulk purification.